## Slide 1
NTUT AIOT LAB · PROGRESS REPORT · AUGUST 2026
Following a Named Object
with Vision and Language
You say what to follow. The drone finds it and chases it.
The guardrail decides where it may not go.
Department of International Graduate Program, EECS
Advisor: Prof. Kuan-Ting Lai · Presenter: Nathanael Cayadi

## Slide 2
HEADLINE
Last report's pilot could not do this. This one can.
Same guardrail, same simulator, same policy files — the pilot changed.
01
Before (AerialVLA 7B)
Now (this report)
Follow a named moving object
no — never moved
yes
Language actually steers
no
yes
Decision rate
0.11 Hz
4–5 Hz
Altitude band held
escaped 31.6 s
0.0 s
No-fly zone
0.0 s
0.0 s
Source: docs/FINDING-what-drives-aerialvla.md, docs/RESULT-vlm-follow.md

## Slide 3
THE FINDING
AerialVLA's language input never reached its output.
108 controlled forward passes per adapter, on real captured frames.
02
12 / 12
flights: identical 'stop and land' output
0.05 vs 0.08
yaw for correct vs WRONG colour word
11 / 18
frames answered LAND with no compass hint
The prompt has two slots. Only one of them steers.
"Fly {direction} and find the target. {object}"
{direction} is a compass phrase computed from ground-truth coordinates — it orders the commanded
yaw monotonically from −0.47 rad/s ("to your left") to +0.16 ("to your right").
{object} is the language. Correct and wrong colour words gave indistinguishable actions.

## Slide 4
THE FIX
We changed the model, not the goal.
Still vision → language → action. Now with a model whose words reach the output.
03
OWL-ViT 153 M
Open-vocabulary detector.
Text in, boxes out.
34–56 ms per frame.
Servo controller
Box offset → yaw.
Box width → speed.
Altitude error → climb.
Guardrail — unchanged
Same Shield, same policies.
No modification needed to
accept a new kind of pilot.
Nothing in the steering path knows where the car is. Its position is used only to spawn it,
and offline, to score the flight.

## Slide 5
THE DEMO
Two flights, one command.
.\run_follow_vlm.ps1
04
1 · Tracking, with stops
The car drives, stops for 6 s, drives,
stops, drives again. The drone has to
stop too — that is the proof.
2 · The same, with a no-fly zone
A fence spans the corridor. The car
drives through it. The drone brakes,
holds at 3 m, and does not.
Recorded from two cameras: the drone's own view with the detection box and live telemetry,
and a third-person chase view, stitched side by side.

## Slide 6
RESULTS
It follows, and the rules hold.
Every row re-flown 2026-08-11. Separation scored offline against ground truth.
05
Condition
Detector hit
Mean sep.
Within 30 m
Shield
NFZ / alt
Follow, car stops twice
99.3%
13.4 m
100%
0
0.0 s
Same again (replicate)
100%
12.5 m
100%
0
0.0 s
+ 3 identical distractors
97.9%
17.7 m
100%
0
0.0 s
Control: wrong colour
22.1%
71.8 m
24.1%
10
0.0 s
No-fly zone across road
100%
38.8 m
34.9%
0
0.0 s
Rows 1 and 2 are the same flight twice — both 100%. Row 3 is the harder task: three MORE cars, same
mesh, only colour differs, so the noun cannot separate them and only the colour test can. Still 100%.
Row 5 is a deliberate failure — the fence spans the whole road, so the car escapes and tracking must
collapse. Zero Shield overrides, because the controller stops itself.

## Slide 7
PROOF
One word decides whether it follows.
Identical scene, identical white car, identical settings.
06
"a white car"
100% of the flight within 30 m
detector hit rate 99.3%
"a red car"
24.1% within 30 m
detector hit rate 22.1%
It does not follow badly — it FAILS TO ACQUIRE. The hit rate collapses from 99.3% to 22.1%, because
the colour gate rejects nearly every candidate outright. The detector grounds the noun; a fixed HSV
rule grounds the adjective. Two different mechanisms, and we say so rather than blur them.

## Slide 8
SAFETY
The guardrail never changed — and it caught a real one.
Not one line of shield.py or any policy was edited for any of this work.
07
0.0 s
in the zone, every flight ever
659 -> 0
Shield overrides, after the fix
NaN
was passing straight through
A safety layer that fails OPEN is worse than none, and ours did.
NaN loses every comparison, so an action carrying one raised zero violations and took the untouched
passthrough branch — reaching the autopilot byte-identical. Infinity was worse: the speed clamp
scales by cap/hypot, and inf times 0 is NaN, so a BOUNDED repair operator manufactured the poison.
Found by a new coverage suite, not by a flight. A non-finite command is now not a command.

## Slide 9
Q: HOW DO THEY CONNECT?
The pilot and the guardrail share one struct.
That contract is why the pilot could be replaced without touching the safety layer.
08
guardrail/models.py
class Action4D:
vx, vy # m/s, North / East
vz_up # m/s, up
yaw_rate # +clockwise
every tick, in the flight loop
raw = Action4D(...) # pilot asks
smooth = limiter(raw)
d = shield.filter(state, smooth)
drone.move_by_velocity(d.emitted)
`raw` never reaches the simulator. Only `d.emitted` flies — the guardrail is the last authority.
Case
Pilot asked for
What actually flew
Rule at risk
Guardrail agrees
vx +0.41 vy −0.62
vx +0.40 vy −0.40
none
Controller brakes itself
vy +0.74
vy +0.74 (unchanged)
none — fence 6.0 m
Guardrail overrides
vx −0.47 toward a wall
vx +0.50
clearance 4.98 < 5.0 m
Real ticks from demo/out/*/flight_log.jsonl. yaw_rate is identical in all three — the Shield never touches heading.

## Slide 10
Q: HOW DOES IT DETECT AND TURN?
From a word to a yaw command, in four steps.
09
1 · Detect
OWL-ViT takes the phrase and returns scored boxes. 34–56 ms, in its own thread.
2 · Verify the colour
HSV check inside each box. The detector grounds the noun, this grounds the adjective.
Winner is score × (0.25 + 0.75 × colour) — not score alone, which once locked onto a building.
3 · Turn
off = (cx − W/2) / (W/2) bearing = 45° × off yaw_rate = gain × bearing
The pixel offset becomes a REAL angle, because it is scaled by the camera's half-FOV.
4 · Close or back off
Box width stands in for distance: too small → forward, too large → reverse.
Scaled by cos(bearing), so it never charges while the target is off to one side.
When detection drops: COAST on the last motion (< 2 s), then SEARCH toward the side it was last seen,
then SCAN slowly. It never freezes, and never-yet-acquired counts as SEARCH rather than give-up.

## Slide 11
LIMITS
What this does not do.
Volunteered, not conceded — each one is measured.
10
1 · The noun is grounded by a network; the colour by a fixed rule.
Nine colour words exist. Anything outside them passes unverified.
2 · It cannot reliably say the object is ABSENT — only at flight level.
75% ABSENT with no target against 40% with one. Per tick it does not separate.
3 · The subject must be SMALL in frame, and it is a simulator.
A 50 m block filled 99% of the image and nothing downstream worked. No hardware yet.

## Slide 12
NEXT
Where this goes.
11
Decisions we need
· Frame contract: ours is world-frame,
upstream is body-frame. Both cannot
be right, and it blocks the flight
controller work.
· COCO: we recommend dropping it,
with the measurements attached.
Work in progress
· Orbit: it now circles a small target,
more than a full lap, but does not
hold its radius.
· Absence: needs more pixels on the
target, not a cleverer rule.
· Then: MAVLink through to ArduPilot.

## Slide 13
TAKEAWAY
The pilot changed completely.
The safety layer did not have to.
A 7B action model was swapped for a 153 M detector and a servo loop — a different kind of
controller entirely — and the Shield accepted it without a single change to its code or its
policy files. Across every flight in this report: no-fly zone 0.0 s, altitude escape 0.0 s.
That portability is the architectural claim, and it survived replacing the brain.
Reproduce: .\run_follow_vlm.ps1 · TUTORIAL-DEMO-FOLLOW.md